ACE Weekly Report : 6/9/99

Monthly status meeting held with Mission Director.  All relevant action items were reviewed.  No significant issues were identified.  The FOT is reviewing a Y2K Business Continuity and Contingency Plan submitted by the DSN.  Comments will be forwarded to the MD by the end of the week.  No major issues are anticipated.

Spacecraft Activities:

- All spacecraft subsystems are performing nominally.

- Successfully performed a two segment attitude maneuver on 6/8 to re-orient the HGA.

Maneuver Start Time=16:09:06     Maneuver End Time=16:12:10  SEGMENT 1

Maneuver Start Time=17:25:03     Maneuver End Time=17:29:27  SEGMENT 2

Pre-Maneuver    HGA = -4.22 deg     Sun Angle =  4.88 deg

Post-Maneuver  HGA = +4.05 deg    Sun Angle =  11.55 deg

Current S/C range:  1,469,746.245   km

Ground System Activities:

- On 6/7 - At ~18:42 data went static fo approximately 1 minute. Station reported alarms with CDR which may have caused problem.  Data resumed with all activities nominal for remainder of the pass.  See DR#N51154 and anomaly report #G99-0042

Instrument Activities:

Weekly SWEPAM calibrations performed successfully on 6/4

Y2K Testing:

- On 6/9 - Started using the MOR string as the prime string for all command, telemetry, and offline activities.  This is the last step of the FOT validation of Y2K software.  The support was executed nominally.  No problems were detected in the operational use of the s/w.  This validation activity is expected to be completed in approximately one week.