ACE Weekly Report : 6/16/99

Period Covered: 6/10/99 to 6/16/99

- Comments to the DSN Y2K Business Continuity and Contingency Plan was forwarded to the Mission Director.  The ACE mission will have no problems adhering to the DSN constraints of not performing any critical activities from year rollover - 12 hours to year rollover +36 hours

Spacecraft Activities:

- All spacecraft subsystems are performing nominally.

- Successfully performed a two segment attitude maneuver on 6/15 to re-orient the HGA.

Maneuver Activities

Maneuver Start Time=19:30:55     Maneuver End Time=20:38:25   (2 parts)

Pre-Maneuver    HGA =  - 4.39 deg     Sun Angle =  5.81 deg

Post-Maneuver  HGA = 4.08 deg  Sun Angle =  12.72 deg

Current S/C range: 1,491,451   km

- Encountered some problems with MOR Attitude Maneuver Command Sheet processing during segment 1 of 2 attitude maneuver planning.  MOPPS software in MOR requires that AC1WS1 be enterered at software startup time.

- Previous versions of S/W did not required user to input workstation for default.  Not entering the workstation caused system to run very slow.   After troubleshooting  it was found that by entering desired wrkstation process speed increased.

- The first segment of the maneuver was executed using a command sheet processed from the MAR.  The second segment of the maneuver was executed using a command sheet processed from the MOR.  This validates the remaining functions of the MORY2K s/w.

Ground System Activities:

overlay of the GRI with 99160 Autonomy dump file

Active C&DH Block bins were dumped and compared using C_BB_DUMP_ACT proc.

- On day 164 (6/13/99) the pass was reduced to 2 hours due to DSN scheduling issues.  The entire recorder was not dumped on that day.  The remaining recorder portions were dumped on the following day, capturing all of the data.

-  On 6/16 Goddard voice experienced keyset failures.  ROLM phone used for communication with D27

Instrument Activities:

- Executed OCR # SWPX-012 to the SWEPAM instrument.  This OCR alllowed the SWEPAM ION team to tune the Ion instrument in order to fine tune solar wind ÒtrackingÓ

function.

-  Monitor of SEPICA instrument Science Telemetry indicated that an alarm (SSSALARMS) had changed from a value of hex 14 to hex 6.  This indicated that Fan 3 pressure had risen high enough for possible science collection.  Instrument representative has been contacted.

-  Executed Sepica command request (OCR SEP-049) to adjust proportional counter output for 2kC High Voltage

Y2K Testing:

- Since 6/9/99 the MOR has been used as the prime string for all command, telemetry, and offline activities.  A maneuver was executed from the MOR on 6/15/99.  System testing for the Y2K s/w is completed.  The FOT will meet with the Y2K team and project personnel to review the results before recommending that the system be declared operational.

Anomalies

G99-0043  MOR Mission Planning Anomaly (user input needed for default workstation) (Described above under maneuver activities).