ACE Weekly Report : 10/5/99

Spacecraft Activities:

All spacecraft subsystems are performing nominally.

Maneuver Activities

Successfully completed an attitude maneuver on 10/12/99. The next attitude maneuver is scheduled for 10/18/99.

Ground System Activities

- No activity to report

Instrument Activities

- 10/8/99 - Executed OCR SEP-055 (part II).   Adjusted Fan 3 2kc setpoint to 97 dec. for change in Fan 3 pressure.

- 10/9/99 – Executed OCR SEP-063.  Adjusted Fan 3 2kc setpoint to 103 dec. for change in Fan 3 pressure.

- 10/10/99 – Executed OCR SEP-055 (part II).  Adjusted Fan 3 2kc setpoint to 97 dec. for change in Fan 3 pressure.

- 10/11/99 – Weekly SWEPAM Electron and ION calibrations performed nominally

Note:  Adjustments of the SEPICA Fan 3 2kc setpoint are needed for collection of valid Science data.

Anomalies

- 10/8/99 – Original support schedule using DSS-66 switched to DSS-27 due to VSOP mission declaring S/C emergency.   No impact to ACE operations.