ACE Weekly Report: 11/10/99

All ACE spacecraft subsystems are performing nominally. An attitude maneuver was completed on 11/08/99. The next attitude maneuver is scheduled for 11/12/99. A Z-axis control maneuver is scheduled for 11/16/99 followed by an attitude maneuver and a spin correction maneuver.

The maneuver on 11/8 was delayed approximately 1 hour when the maneuver command sheet failed to be processed through MOPSS. An error message suggested that the command sheet already existed. The software was recycled twice and the command sheet retransmitted. The error message was no longer received but the command sheet processing failed again. The backup for MOPSS is on the prime string. It took several attempts to successfully process the command sheet on the prime string following some database connection errors. The database connection errors were received because the ORACLE instance for that particular database was not active. Follow up investigation of the MOPSS error message by a MOPSS developer/tester revealed that a failure during processing had created a private schedule with the same name causing the processing to hang. The solution is to check for private schedules and delete these using the existing "Delete Schedule" function.

On 11/9/99, unusual yellow limit violations were seen for the SWEPAM instrument undercount alarm. The instrumentor was contacted and the FOT was informed that the alarms were due to the low sample rate by the instrument CEM supply possibly arising from low solar wind activity.

Contingency simulations have progressed and will continue through the end of the week as part of Leonid preparations.