ACE Weekly Report: 12/22/99

All ACE spacecraft subsystems are performing nominally. A successful attitude maneuver was completed on 12/21/99.  Upcoming attitude maneuvers are scheduled for 12/28/99 and 01/06/2000.

# S/C Activities

12/16/99

Executed Block Bin dump and compare of the active C&DH (A) with no miscompares.

12/18/99

Scrolled through telemetry sections of Solid State Recorder to check for Single Bit Errors.

12/19/99

Executed Inactive C&DH (B) Block Bin dump.  Bins recorded on SSR and played back for compare.

12/20/99

Executed Weekly SWEPAM instrument calibrations.

Executed instrument OCR for SEPICA (SEP-068) to adjust Fan 3 2kc set-point to compensate for change in Fan 3 pressure.

# Other Activities

FOT has created 2 procedures for Loading and Clearing a Time Tag Bin to execute the C&DH Last Resort Timer  (LRT) poke command in preparation of any prolonged Y2K ground communication interruptions.   FOT has created S/C Operational Change Request and is awaiting approval for implementation.