ACE Weekly Report: 02/16/2000

All ACE spacecraft subsystems are performing nominally.

Pass activities for the lissajous Z-axis control maneuver (LZCM) have been ironed out. Five instruments (SWEPAM E&I, SWICS, SWIMS, and ULEIS) will ramp down high voltages on Wednesday 02/16/00.

On Thursday, 02/17/00, the spacecraft RF subsystem will be reconfigured for the low rate broad-beam antennas. This RF configuration will be required throughout the entire pass for all maneuvers and so no SSR data recovery is expected but will be provided on a best effort basis. The maneuvers scheduled for 02/17/00 are: Attitude reorientation - 1 (ATT REOR-1), LZCM-2 segment 1, LZCM-2 segment 2, ATT REOR-2. Each of these maneuvers will be followed by approximately 1 hour of nutation damping and attitude re-determination. At the end of the day, a spin rate burn will be executed and the RF subsystem will be reconfigured for the High Gain Antenna (HGA).

The first pass scheduled for Friday 02/18/00 will be used to dump the SSR and ramp up as many instrument high voltages as time permits. The second pass will be used to perform the station-keeping maneuver and another attitude reorientation maneuver as well as SSR data recovery.

Ground System Anomalies: On 02/15/00, Big pipe went down for 1 minute and 42 seconds resulting in a need to replay SSR-A slices 405-415. See DR#G05784 and anomaly report #G00-0006.