ACE Weekly Report : 5/4/99

- The upgrade of the MAR string to Y2K software is completed.  The MAR has been used as the prime string for all contacts since April 22.  DSN has completed its transition to the Y2K system (SFG, Routers, etc.).  A new INIF patch was installed in the MAR and in the GAS (INIF R2c) on 4/29/99 to fix problems that were encountered during testing of INIF R2b.  Currently both INIF R2b and INIF R2c are installed on both systems.  The old INIF version (non-Y2K compatible) has been deleted.  Starting on 4/30/99 the INIF R2c is used for all real-time contacts.  Once INIF R2c is fully verified, all other versions will be removed from the system.  Two ACE strings are now Y2K compliant and operational.

- Upgrade of the MOR system to Y2K started on 5/3/99.  A streamlined implementation plan, based on the one used for the MAR, has been developed to upgrade the MOR.

- Successfully performed an attitude maneuver on 4/30/99.

Pre-maneuver: sun angle = 10.87 deg, HGA = -4.23 deg, spin rate = 4.975 rpm

Post-maneuver: sun angle = 5.54 deg, HGA = 4.48 deg, spin rate = 4.976 rpm

- All spacecraft subsystems are performing nominally.

- NOAA contacted FOT on two consecutive days (123 and 124) to report that telemetry was not received at the beginning of the support.  The IPNOC restarted the ISIS process for NOAA each time and the problem was resolved.

- DSN Ground Anomaly

G99-0036 - DR#G04864 - The DSN Transmitter PAT voltage turned itself off.  This caused the receiver to go from 2 to 1-way as well as caused loss of telemetry.  There was an approximate 3 minute telemetry dropout in MOC.

No ranging data was received in the MOC for approximately 1 minute on day 117.  Ranging data "red" between 14:44 and 15:48 covered by DR# G04855