ACE Weekly Report : 7/29/99

Spacecraft Activities:

- All spacecraft subsystems are performing nominally.

Maneuver Activities

- Performed a nominal attitude maneuver on 7/26/99

Maneuver Start Time=14:44:17    Maneuver End Time=14:51:06

Pre-Maneuver    HGA = -3.56      Sun Angle =  4.0

Post-Maneuver  HGA = 4.49     Sun Angle =  11.05

Current S/C range:  1,577,050   km

Ground System Activities:

- 7/27/99 -  Due ot operations by the CHDR Satellite, original support time was moved from a nominal 3.5 support on D16 to a 2 hr and 40 minute support on D61.  SSR operations unable to be completed due to shortened support (collected 568 of 636 slices)  This remaining data will be collected on next support.

- Completed playback of SSRB remaining slices on 7/28/99

Instrument Activities:

-  Weekly SWEPAM calibrations were performed on 7/23

Anomalies

On 7/21/99 at ~17:14, DSS-27 notified MOC that the CPA had rejected a command received at 17:13:18. The MOC advised station that no commanding was being performed at that time. Station brings command carrier down at the request of the MOC. MOC requests that the Ops Chief investigate.  The Ops Chief was not able to identify the point of origin of the extraneous commands.  All the suspicious commands were rejected at the station and were not transmitted to the s/c.   The incident is documented in anomaly report #G99-0046.  An IT security breach incident report was also filed.