ACE Weekly Report : 8/26/99

Spacecraft Activities:

- All spacecraft subsystems are performing nominally.

Maneuver Activities

- No maneuvers performed this week.  The next attitude maneuver is scheduled for 8/30/99.

Instrument Activities

- 8/23/99 - SWEPAM weekly calibrations performed successfully.

Anomalies

- 8/19/99 - CPA swap out performed (DR L03564) - No impact to ops. AR G99-0047

- 8/20/99 - During Support Transmitter  at D16 went red.  D16 informed ops crew that Antenna would need to be placed in stow position for Power amp recycle.   DSS 27 was brought up and support continued for SSR playback and end of day  command ops.

AR G99-0048  - DSN Transmitter problem  (DR # G05214)

- 8/22/99 - Approx 45 minutes prior to BOT, ISIS protos server crashed and was down for 15 minutes. (no impact to ops)

General

- Prepared mission status package for receiving review for transferring of mission  management responsibility between GSFC codes.  Conducted review of package with MD.  Package will be update to reflect changes.

- Reviewing Y2K contingency plan document.  Comments have been submitted to the document lead.

Anomaly Closures

- Review of anomaly reports continues.  The 1998 Ground System anomalies were reviewed.  159 ground system anomalies were opened in 1998.  158 (Numbered G98-0001 to G98-0255) have been closed (Some numbers were skipped in the sequence).  One ( # G98-00064) remains open for further investigation.  The anomalies closed dealt mostly with G/S software problems (like the packet extractor crash) which have been fixed by the current version of the s/w and with DSN scheduling and equipment problems.  A new process was  put in place for the scheduling problems and it has resolved the predict problems that were causing the scheduling anomalies.  The anomaly closure report will be distributed at the ACE montly meeting.