ACE Weekly Report : 9/22/99

Spacecraft Activities:

All spacecraft subsystems are performing nominally.

Maneuver Activities

Successfully completed attitude maneuver on 9/17/99.  The next attitude maneuver is scheduled for 9/27/99. The next stationkeeping maneuver with a spin maneuver has been re-scheduled for 10/4/99 to allow for all activities to be completed during the nominal pass time. An attitude maneuver will follow on 10/5/99.

Ground System Activities

- 9/20/99 - JPL/DSN performed a RNS/SCP Emulator Test which involved switching ACE to the new system at 1620. Minor dropouts were observed and expected but did not impact data recovery.

Instrument Activities

- 9/16/99 - 9/18/99 A current violation (detected by configuration monitor) caused the S3DPU to turn off the SEPICA 30kv supply. The instrumenter was contacted in accordance with the ACE Escalation Procedures. OCR SEP-020 was executed in steps over the course of 3 days to restore the 30kv supply to the operating voltage.

- 9/20/99 - Weekly SWEPAM calibrations performed successfully

- 9/21/99 - Executed OCR SIS-011 to calibrate the instrument.

Anomalies

- 9/19/99 - Big Pipe failure.  Replayed recorder in the blind; playback data was recorded at station and will be transmitted to CDR when big pipe is back up. No DR# given, skipped bin dumps at end of day due to sporadic VC1 dropouts. CDR file played back successfully on 9/20/99 to recover SSR data.

- 9/20/99 - Packet Extractor appeared to fail. See anomaly report G99-0057. No data was lost.