ACE Weekly Report : 9/29/99

Spacecraft Activities:

All spacecraft subsystems are performing nominally.

Maneuver Activities

Successfully completed attitude maneuver on 9/27/99.  The next stationkeeping maneuver with a spin maneuver is scheduled for 10/4/99 . An attitude maneuver will follow on 10/5/99.

Ground System Activities

9/20/99 -

Instrument Activities

9/23/99 - 9/24/99 - Executed OCR SIS-011 to calibrate the instrument.

9/27/99 - Executed instrument OCR SIS-012  instrument is still testing response time of instrument to gain knowledge of optimum instrument configuration for improving the return of helium events.

9/27/99 - 9/28/99 - Executed instrument OCR SEP-020; During the weekend SEPICA 30 Kv voltage was again reset by S3DPU due to high current violation.  This reset occassionally happens,and is due to onset of corona which might precede a discharge.

9/28/99 - Executed four instrument OCR's:  1) Completed final day of testing for SIS (OCR SIS-012) used for determining optimum instrument configuration for helium events.  2) Executed SWPX-017 for SWEPAM Electron instrument CEM level adjust from 9 to 10. 3) Executed OCR SEP-020 (continuation from previous day for recovery ops from 30 kv reset from the weekend.  OCR has not been completed.  Instrumenter ramping the 30 kv up slowly over a couple of days. 4)  Executed OCR SEP-059 to adjust Fan 3 2kc setpoint due to pressure change in Fan #3.  Fan 3 pressure had risen too high for science collection.  Adjustment put science data back online.

9/29/99 - Executed OCR SEP-020 to recover from 30 kv reset.  30 kv volatage at ~23.8. Executed OCR SEP-060 to adjust the Fan 3 2kc setpoint. OCR SEP-020 Pt II to be executed on day 273 to raise 30kv voltage at stop point of ~27 v

Anomalies

9/24/99 - Delayed AOS due to antenna problems at D61. See Anomaly Report G99-0058 and DR#L03834

9/26/99 - DSS-66 unable to support pass due to a transmitter failure. Support changed to DSS-27. See DR #L03648 and anomaly report #G99-0059.

9/27/99 - DSS 66 declared red prior to support.  Support was achieved on DSS-27.   Successfully performed attitude manuever using D27.  It was noted that Doppler ranging can be achieved using D27 for FDF analysis..

9/28/99 - Experienced RFI affecting Goldstone complex DSS -27 which impacted approx 32 minutes worth of SSR playback.  Remaining SSR data will be collected on next support (approx 16 min).  (DR G05340)