ACE Weekly Report: 02/09/2000

All ACE spacecraft subsystems are performing nominally.

A successful attitude maneuver was completed on 02/08/00.  Upcoming attitude maneuvers are scheduled for 02/17/00, 02/18/00, and 02/29/00. A Z-axis lissajous control maneuver is scheduled for 02/17/00 with a station-keeping maneuver to follow on 02/18/00. This will require a significant amount of contact time and so a longer 9+ hour DSN support is scheduled for 02/17/00 and a combination of two supports are scheduled on 02/18/00 lasting 9 hours. Some other non-nominal activities that are planned to occur during the z-axis maneuver time frame include: instrument ramp downs and ramp ups, RF reconfigurations to the low rate broad beam antennas and back to the high gain antenna, and SSR management activities.

On 02/02/00, AOS was delayed approximately 9 minutes due to station transmitter interface problems (DR #G05754). Also on this day, a SEPICA instrument alarm was triggered that indicates a current transient in the 30kv supply. Other telemetry indicated that a discharge did not occur. The instrumenter was notified and the alarm flag was cleared with OCR SEP-071.

TPOCC software fixes (DR fixes and a FORMATS subsystem change) are being installed in the Ground Analysis Support facility this week.

A plan has been put together to utilize some external hard disk drives that were not in use. This plan will repartition the hard drives to increase trending and real-time ops data storage capabilities.