ACE Weekly Report: 0413/2000

All ACE spacecraft subsystems are performing nominally. Successful attitude maneuvers were performed on 04/06/00 and 04/14/00. The next attitude maneuvers are scheduled for 04/18/00, 04/24/00 and 04/28/00.

DSN 26m Automation Test performed with Station D16 on 04/08/00.  ACE successfully received s/c telemetry as well as monitor data from the site.  However telemetry receipt was delayed ~45 minutes due to facility codes not being enabled at site.  Commands were also successfully sent to both the Active and Inactive C&DHs.  ACE has yet to validate the receipt of Sequential ranging data;  this function is not ready to be tested.

On 04/11/00, CPA rebooted following CPA failure; no impact to real-time operations.

See AR# G00-0011:  DR# G05867.

On 04/12/00 telemetry lost for ~8 minutes due to ISIS problem; IPNOC resolved in real-time.  All affected SSR slices redumped during the support. See AR# G00-0012.