ACE Weekly Report:  06-07-00

All ACE spacecraft subsystems are performing nominally. An Attitude maneuver was successfully executed on 06-02-00.  The next attitude maneuvers is scheduled for 06-09-00.

On 06-02-00 an obsolete thruster setup command was uploaded to the spacecraft.  The error was

caught before it was to be manually executed.  The setup command was cleared and the necessary clean up performed.  The correct thruster setup was then uplinked and successfully executed.

AR G00-0023 can provide additional details.  The FOT is currently applying the Root Cause and Corrective Action (RCCA) process to determine the ‘true causes of the event, identify and implement corrective actions and assess the effectiveness of the corrective actions in preventing the recurrence of the event’.  All findings will be made available upon its completion.

On 06-04-00 AOS  was delayed ~10 minutes due to transmitted problems at Station 66.  All SSR data was successfully captured and daily activities were completed by the scheduled EOT.  See

AR G00-0024 [DR #L04384] for additional information.